## Slide 1: Transmission Impairment

## Slide 2: Transmission Impairment
The signal that is received may differ from the signal that is transmitted due to various transmission impairment.
Consequences
  For analog signals, these impairments can degrade the signal quality.
  For digital signals, bit errors may be introduced, such that a binary 1 is transformed into a binary 0 or vice versa.

## Slide 3: Impairment Causes
Transmission Impairments
Attenuation
Distortion
Noise
The imperfections of the medium causes impairments in the signal. What are the possible impairments? First is the attenuation, then distortion and noise.

## Slide 4: Transmission Impairment considerations
Attenuation introduces three considerations for the transmission engineer.
  First, a received signal must have sufficient strength so that the electronic circuitry in the receiver can detect the signal.
  Second, the signal must maintain a level sufficiently higher than noise to be received without error.
  Third, attenuation varies with frequency

## Slide 5
The first and second problems are dealt with by attention to signal strength and the use of amplifiers or repeaters.
The third problem is dealt with equalizing attenuation across a band of frequencies. Another approach is to use amplifiers that amplify high frequencies more than lower frequencies.

## Slide 6: Attenuation: the loss of energy as the signal passes through a medium. Unit of measurement: Decibel
Figure refer by Techterm youtube channel

## Slide 7: Amplifier
Figure refer by Techterm youtube channel
An amplifier can be used to compensate the attenuation of the medium

## Slide 8: Unit to measure Strength is Decibel(dB)
Figure refer by Techterm youtube channel
dB = 10log10 P2/P1
Where,
P2 is the power at the destination or point 2
P1 is the power at the transmitting end or point P1.

## Slide 9: A signal travels through a transmission medium and its power is reduced to one half. Calculate the Attenuation
P2 = 0.5 P1
dB = 10 log 10(P2/P1)
= 10 log 10(0.5 P1/P1)
= 10 log 10(0.5)
= 10 *(-0.3010)
= -3dB (Approx)
P1
P2
Transmission medium

## Slide 10: A signal travels through a amplifier and its power increased 20 times. Calculate the power gain
P2 = 20 P1
dB = 10 log 10(P2/P1)
= 10 log 10(20 P1/P1)
= 10 log 10(20)
= 10 *(1.301)
= 13dB (Approx)
P1
P2

## Slide 11: Delay distortion
Delay distortion arises particularly in a guided media but not in air.
Delay distortion arises because velocity of propagation varies with frequency.
That means this signal components that we are sending will have different velocities for different frequency components as it passes through a guided media and this leads to delay distortion.

## Slide 12: Delay distortion (contd…)
Because of delay distortion, some of the signal components of one bit position will spill over into other bit positions, causing intersymbol interference
1000101010001001
Equalizing techniques(Delay Equalizer) can also be used to avoid delay distortion.

## Slide 13: Noise
unwanted signals that are inserted somewhere between transmission and reception.
undesired signals are referred to as noise.
Noise is the major limiting factor in communications system performance.

## Slide 14: Noise
Original Signal
Noise Signal
receiver side the sender signal combine with nois

## Slide 15: Noise
Noise may be divided into four categories:
Noise
Thermal
Intermodulation
Crosstalk
Impulse

## Slide 16: Noise Type1: Thermal Noise (White noise)
Random motion of electrons in wire creates extra signal which is not sent by transmitter
Due to random motion of electrons.
Present in all transmission devices and media
is a Function of temperature
A kind of noise where the irregular electron movement in wire produces an additional signal.
Thermal noise is uniformly distributed across the bandwidths and hence is often referred to as white noise

## Slide 17
1°C + 273.15 = 274.15K
17°C + 273.15 = 290.15K

## Slide 19: Noise Type2: Intermodulation Noise
When signals at different frequencies share the same transmission medium, the result may be intermodulation noise.
The effect of intermodulation noise is to produce signals at a frequency that is the sum or difference of the two original frequencies or multiples of those frequencies.
For instance, consider two signals S1 and S2 generate signals of frequencies (S1 + S2) and (S1 - S2) that may interfere with the signals of the same frequencies sent by the sender. In any part of the communication system, intermodulation noise is introduced because of this situation.
Intermodulation noise is produced by nonlinearities in the transmitter, receiver and/or intervening transmission medium.

## Slide 20: Noise Type3: Cross Talk
crosstalk is due to unwanted coupling between two media.
In telephone network, we frequently encounter crosstalk.
We hear some unwanted talk going on in the background. This is because of this unwanted coupling between two transmission media that means cables.
It can occur by electrical coupling between nearby twisted pairs or rarely coaxial cable lines carrying multiple signals

## Slide 21: Noise Type4: Impulse noise
All of the types of noise discussed so far have reasonably predictable and relatively constant magnitudes.
Thus, it is possible to engineer a transmission system to cope with them.
Impulse noise, however, is noncontinuous, consisting of irregular pulses or noise spikes of short duration and of relatively high amplitude.
It is generated from a variety of causes, including external electromagnetic disturbances, such as lightning, and faults and flaws in the communications system.

## Slide 23: Channel Capacity
The maximum rate at which data can be transmitted over a given communication path, or channel, under given conditions, is referred to as the channel capacity.
There are four concepts here that we are trying to relate to one another.
  Data rate : The rate, in bits per second (bps), at which data can be communicated
  Bandwidth: The bandwidth of the transmitted signal as constrained by the transmitter and the nature of the transmission medium, expressed in cycles per second, or Hertz
  Noise : The average level of noise over the communications path
  Error rate : The rate at which errors occur, where an error is the reception of a 1 when a 0 was transmitted or the reception of a 0 when a 1 was transmitted
  Two theoretical models: (Calculate Data rate)
  Nyquist Capacity : assumes noise-free environment
  Shannon Capacity : considers noise

## Slide 24: Nyquist Capacity
Assumes channel that is noise free
Given a bandwidth of B, the highest signal rate is 2B
Single signal element may carry more than 1 bit; signal with M levels may carry log2 M bits
C = 2B log2M
Where, B is Bandwidth, M is the number of discrete signal or voltage levels.
Tradeoffs:
  Increase the bandwidth, increases the data rate.
  Increase the signal levels, increases the data rate.
  Increase the signal levels, harder for receiver to interpret the bits (practical limit to M)

## Slide 25
For a given bandwidth, the data rate can be increased by increasing the number of different signal elements(M).
However, this places an increased burden on the receiver:
  Instead of distinguishing one of two possible signal elements during each signal time, it must distinguish one of M possible signal elements.
  Noise and other impairments on the transmission line will limit the practical value of M.